## Slide 1
Real-time alignment of the LHCb RICH detectors
Primary mirrors
Secondary mirrors
Detector plane
Ring Imaging Cherenkov detector:
If mirrors are misaligned, the Cherenkov angle is reconstructed incorrectly => bad PID 
Alignment Procedure: data driven, iterative
Reconstruct selected
events
Current alignment
Has the alignment changed?
Amend alignment constants
Run I: offline alignment after data-taking, twice a year (?) => reprocessing of data
Run II: real-time alignment every fill!!!
L0 Trigger
HLT1
buffer
Calib.
HLT2
Offline
Implementation on HLT farm:
Central Node
Farm Node
Farm Node
Alignment Constants
Alignment Constants
Results
Results
…
Alignment Constants
~1800 Nodes
Event Data
Event Data
Farm Node
~1800 farm nodes used for event reconstruction
Central node evaluates results from reconstruction and calculates new alignment constants
Everything steered by a Finite State Machine
Super fast! :D
NEW!