## Slide 1
Novel Real-time Calibration and Alignment Procedure for LHCb Run II
Claire Prouve, on behalf of the LHCb collaboration University of Bristol
LHCC - 02 March 2016 - Poster Session
xxx
Increase in energy: √s = 7(8) TeV ⇒ 13 TeV
15% increase of inelastic collision rate
20% increase of multiplicity per collision
60% increase of σbb ̄ and σcc ̄
Reduced bunch spacing: 50 ns ⇒ 25 ns
New challenges in Run II
xxx
Particle identification useable in the high level trigger
Overall improved trigger efficiency
Stable quality of alignment
No more differences between online and offline
ccc
Alignments performed for each fill
trigger line for each task
Event reconstruction parallelised on analysers (1700 nodes), computing of alignment constants by iterator (1 node)
Steered by the run control using a Finite State Machine
VELO, Tracker & calibrations: automatic update of the constants if they differ by a given value
RICH alignment & Muon System: monitoring mode
Real Time Alignment and Calibration
Alignment Farm and Framework
xxxsssss
Position of the tracking elements in x and y
Minimisation of residual of Kalman track fit using additional constraints
Independent alignments:
  VELO & Tracker: updated every O(1) fills
  Tracker: updated every O(1) weeks
  Muon system: updated O(1) per year
  ~7 minutes for each task
Tracker Alignment: VELO, Tracker, Muon System
Orientation of the RICH mirrors in x and y
Fit the variation of the Cherenkov angle Δθ as a function of the polar angle ϕ to extract the misalignments on the detector plane (Θx, Θy):
Δθ = Θx sinϕ+ Θy cosϕ
Monitoring mode, updated O(10) times a year
~30 minutes per task
Refractive index calibration: Fit to the reconstructed-expected Cherenkov angle yields scale factor for the refractive index
HPD image calibration: Sobel filter applied to each HPD and used to provide calibration
Updated every run
RICH Calibration
ccc
Relative calibration for each cell
Scale the High Voltage by factor α to keep the gain stable by evaluating the variation of the occupancy
  LED monitoring system to detect ageing of the Photo Multiplier Tubes
Updated per fill
Calibrate to the neutral π mass
Fit the π0 mass distribution for each cell for π0 γγ, where one γ has its seed in the cell
Run on the HLT-farm during TS
Calorimeter Calibration
xxx
Global time alignment for all modules
Fit the residual of the drift time to extract the global time delay t0 caused by readout electronics
  tmeas = t0 + tflight + tdrift + tprop
Updated every O(10) runs
Outer Tracker Calibration
Performance and Impact on Physics
Performance of LHCb Detector
PID efficiency
Decay-time resolution
Mass resolution
PID impact D+→π+π-
Example of alignment sequence
LHCb Trigger Schemes
First alignment
Improved alignment
RICH Mirror Alignment
Without PID
With PID
σΥ(1S) = 86 MeV/c2
σΥ(1S) = 44 MeV/c2
Misaligned mirrors
Aligned mirrors
Azimuthal angle ϕ
Azimuthal angle ϕ
Cherenkov angle
Cherenkov angle
HPD image
RICH1 Stability
VELO Stability
Run number
OT Stability
π0 calibration
RICH1 scale factor
LED average
Tracking efficiency
Trigger
+PID
+tighter PID
PID efficiency
signal pT[MeV]
References:
[1] R. Aaij et al., Int.J.Mod.Phys. A30, 1530022 (2015). [2] R. Aaij et al., JINST 9, 09007 (2014). [3] J. Amoraal et al., Nucl.Instrum.Meth. A712, 48 (2013).
[4] M. Adinolfi et al., Eur.Phys.J. C73, 2431 (2013). [5] W. Hulsbergen, Nucl.Instrum.Meth. A600, 471 (2009). [6] R. Arink et al., LHCb-DP-2013-003.
Run number
Bs0 →Ds- π+
Dimuon resonances
Trigger efficiency: Run I and Run II