## Slide 1
09/09/2016 Claire Prouve - University of Bristol
Alignment and Calibration report
on behalf of the Alignment & Calibration group

## Slide 2: Overview
Perform alignment and calibration of subdetectors ‘in real-time’
 Same constants in the trigger and the offline reconstruction
 Use of PID information in HLT2
 Best possible trigger performance
Requirements: fast + evaluated in real-time
Buffer events to disk before running HLT2
Alignments + π0 calibration:
  Use HLT farm with ~1800 nodes
Collect results on single node and evaluate the alignment constants
Calibrations:
Run on monitoring histograms

## Slide 3: Overview

## Slide 4: VELO alignment
Giulio,
Silvia
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per fill | Min. bias + beam gas events | 5 min. | 2 min
Alignment of both halves for translations and rotations in x, y and z.
Stable running since beginning of Run II
Alignment constants updated every 2-3 fills

## Slide 5: VELO alignment
Giulio,
Silvia
Study on alignment of individual modules:
Module misalignment can degrade alignment if 4 - 8μm in Tx, Ty
Alignment of modules for main degrees of freedom: Tx, Ty and Rz
4 fills from the beginning of 2016 data taking
 Compatible with statistical fluctuations, no frequent modular alignment needed.
Study on χ2 convergence criteria:
Convergence reached if χ2 /ndof < 2
Update of alignment constants dependent on change in constants
Plot the variation of the alignment constants as a function of χ2 /ndof
 All triggered updates have χ2 /ndof > 200
Tx[mm]
χ2 /ndof

## Slide 6: Tracker alignment
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per fill | D0 sample | 12 min. | 7 min
Alignment of each IT, TT and OT box for translations in x and z and IT boxes for rotations in z (online) and translations and rotations around y (offline).
Francesca, Lucia, Maurizio, Wouter
Stable running since beginning of Run II
Alignment constants updated every 4-5 fills
Internal alignment performed manually at the start of the year using Zμμ tracks from 2015 data

## Slide 7: Tracker alignment
To be done:
Evaluation of alignment with high momentum tracks and tracks from J/Ψ events
Study different alignment configurations
Stability study for IT: correlation between movement seen by BCAM (Pavol's talk) and tracker alignment under study
Stability study for OT and TT: stability of alignment constants of the different elements
Plans for 2016 data-taking
Detector was opened and IT2C box was moved (~1mm in x,y)  expect significant misalignment at the start
1st alignment with big data-sample and all degrees of freedom at the beginning of data-taking
Alignment in y with magnet-off data
Use D0 events plus high-momentum tracks (and possibly J/Ψ events)
IT1 A side X-coordinate
IT1 C side X-coordinate s

## Slide 8: Muon alignment
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Monitoring mode only | Per fill | J/ψ sample | 3 hours | 7 min
Alignment of both halves of each station for translations in x and y.
Stable running since beginning of Run II
First alignment 2016:
  Misalignment of M1 of ~2mm in Tx  mechanically moved
  New condDB release and LUT for L0 produced
Stable conditions with variations well below required precision of 1mm
Silvia,
Stefania

## Slide 9: RICH Mirror alignment
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Monitoring mode only | Per fill | HLT1 line | 1.5 hours | 30 min (both RICHs)
Alignment of each mirror for rotations about local y and z axes.
Automatic running since beginning of 2016
Alignment constants updated at the beginning of data taking this year
Anatoly,
Claire,
Paras

## Slide 10: OT Calibration
Philippe,
Lucia
Calibration of global time delay caused by a difference in collision time and the phase of the LHC clock received at LHCb t0 (online) and time differences between different OTIS chips tOTIS(offline).
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per run | Min. bias | O(min) | O(min)
Stable running since beginning of Run II
Offline calibration for each tOTIS applied, only expected to change due to hardware interventions  perform ~once a year
Resolution improved from 3ns in Run I to 2.43 ns (Monolayer alignment + global t0 calibration) 2.40 ns (Monolayer alignment + global t0 calibration + offline tOTIS calibration)
 DB update for condDB and simulation with new resolution planned

## Slide 11: RICH calibrations
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per run | HLT1 line | 15 min | O(min)
Calibration of refractive index and HPD image shift.
HPD image w/o and w/ Sobel filter
Chris,
Jibo

## Slide 12: Calorimeter Calibration
Marie-Noelle,
Jean Francois
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per fill | Min. bias | O(1h) of LED data | O(min)
LED calibration of the gain of the photomultipliers.

## Slide 13: Calorimeter π0 Calibration
Dasha,
Jean Francois
Update of constants | Frequency | Data sample | Time to collect data | Time to run
No | ~1 per month | Min. bias | 3-4 days | 5 hours
Calibration by fitting the Pi0 mass for each calorimeter cell.

## Slide 14: Conclusion
Many studies done during WS
Improvements in performance
Improvements in speed
Some small improvements/studies still to be made
Further work on the monitoring required
Getting ready for data-taking!