## Slide 1
09/09/2016 Claire Prouve - University of Bristol
Alignment and Calibration report
on behalf of the Alignment & Calibration group

## Slide 2: Overview
Perform alignment and calibration of subdetectors ‘in real-time’
 Same constants in trigger and offline reconstruction
 Use of PID information in HLT2
 Best possible trigger performance
Requirements: fast + evaluated in real-time
Alignments + π0 calibration:
  Use HLT farm with ~1800 nodes
Collect results on single node and evaluate the alignment constants
Calibrations:
Run on monitoring histograms
Manual, offline, hardware alignments

## Slide 3
Alignments

## Slide 4: VELO Alignment
Giulio,
Silvia
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per fill | Min. bias + beam gas events | 5 min. | 2 min.
Alignment of both halves for translations and rotations in x, y and z.
Running since beginning of Run II
Alignment constants updated every 2-3 fills
Stability studies:
  Threshold for automatic update of alignment constants
  Dependence on initial alignment
  [LHCb Week March 2016]

## Slide 5: VELO Alignment
Giulio,
Silvia
Study on alignment of individual modules:
Module misalignment degrades alignment
Align modules for main DOF: Tx, Ty and Rz
 Compatible with statistical fluctuations, no frequent modular alignment needed.
Study on χ2 convergence criteria:
Convergence if χ2 /ndof < 2
Update of constants dependent on variation
Plot the variation against χ2 /ndof
All triggered updates have χ2 /ndof > 200
Studies on the impact of residual mis-alignment on physics ongoing [Matej Roguljic's talk]
Tx[mm]
χ2 /ndof

## Slide 6: Tracker Alignment
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per fill | D0 sample | 12 min. | 7 min
Alignment of each IT, TT and OT box for translations in x and z, rotations in x , IT boxes for rotations in z (online) and translations and rotations in y (offline).
Francesca, Lucia, Maurizio, Wouter
Running since beginning of Run II
Alignment constants updated every 4-5 fills
Studies:
  Optimisation of thresholds for automatic update
  Optimisation of DOF used online
  Offline alignment for Ty performed on mag off data at the beginning of the year [LHCb Week June 2016]

## Slide 7: Tracker Alignment
Study on using Z  μμ for internal alignment:
OT modules split above/below the beam pipe, OT C-frames in z, split TT modules, IT boxes, IT layers and ladders
Performed on 2015 data
Applied from beginning of 2016
Using CALIBOFF database in DaVinci prepared by Wouter [Wouter's talk] on 2015 data [Stephen's talk]
15% improvement in Z mass resolution
Smaller variation of Z mass with Φ(μ)
Stephen, Wouter

## Slide 8: Hardware Tracker Alignment
Using light + mask/reflector + camera to track points
BCAM: [Pavol's talk]
1 per C-frame of each IT station
every 18 sec
Integrating over 1h  5μm precision
RASNIK: [Artur's talk]
4 per C-frame of each OT station + 2 on bridge
Precision up to 5μm
Movement seen also by software alignment  real movement of the bridge
Work on relating BCAM with RASNIK with software alignment ongoing
Use BCAM/RASNIK as constraints for software alignment(?)
IT1 C-side in z
Bridge Q13
Fred, Pavol Artur, Niels

## Slide 9: RICH Mirror Alignment
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Monitoring mode only | Per fill | HLT1 line | 1.5 hours | 30 min (both RICHs)
Alignment of each mirror for rotations about local y and z axes.
Manual running since mid 2015
Automatic running since beginning of 2016
First alignment 2016 into new condDB release
  Improvements during Run II:
    Increase in speed from 4 hours to 15 min per alignment
    Increase in stability [LHCb Week March 2016]
Anatoly,
Claire,
Paras

## Slide 10: RICH Mirror Alignment
Anatoly,
Claire,
Paras
RICH2 secondary mirrors in y
RICH2 secondary mirrors in z
RICH2 primary mirrors in y
RICH2 primary mirrors in z
Run I:
0.68 mrad
Run II:
0.66 mrad
Well within required precision!

## Slide 11: RICH Mirror Alignment
Anatoly,
Claire,
Paras
RICH1 secondary mirrors in y
RICH1 secondary mirrors in z
RICH1 primary mirrors in y
RICH1 primary mirrors in z

## Slide 12: RICH Mirror Alignment
Anatoly,
Claire,
Paras
RICH1 secondary mirrors in y
RICH1 secondary mirrors in z
RICH1 primary mirrors in y
RICH1 primary mirrors in z
DOWN
UP
DOWN
DOWN
UP
DOWN
Small difference due to mag polarity.
 No visible impact on overall resolution/performance

## Slide 13: Muon Alignment
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Monitoring mode only | Per fill | J/ψ sample | 3 hours | 7 min
Alignment of both halves of each station for translations in x and y.
Running since beginning of Run II
First alignment 2016:
  Misalignment of M1 of ~2mm in Tx  mechanically moved
  New condDB release and LUT for L0 produced
Stable conditions with variations well below required precision of 1mm
[Stefania's talk]
Silvia,
Stefania

## Slide 14
Calibrations

## Slide 15: OT Calibration
Philippe,
Lucia
Calibration of global time delay caused by a difference in collision time and the phase of the LHC clock received at LHCb t0.
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per run | Min. bias | O(min) | O(min)
Running since beginning of Run II
Offline calibration for each tOTIS applied, change only due to hardware interventions  perform ~once a year
Resolution from 3ns in Run I to: 2.43 ns (Monolayer alignment + global t0 calibration) 2.40 ns (Monolayer alignment + global t0 calibration + offline tOTIS calibration)
 DB update for condDB and simulation with new resolution planned

## Slide 16: RICH calibrations
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per run | Mon. histogram | 15 min | O(min)
Calibration of refractive index and HPD image shift.
HPD image w/o and w/ Sobel filter
Chris,
Jibo
Stable running since beginning of Run II
All works well, nothing to report!

## Slide 17: Calorimeter Calibration
Marie-Noelle,
Jean Francois
Update of constants | Frequency | Data sample | Time to collect data | Time to run
Automatic | Per fill | LED data | O(1h) | O(min)
LED calibration of the gain of the photomultipliers.
Running per few fills since beginning of Run II
Running per fill since beginning of 2016  more stable gain

## Slide 18: Calorimeter π0 Calibration
Dasha,
Jean Francois
Update of constants | Frequency | Data sample | Time to collect data | Time to run
No | ~1 per month | Min. bias | 3-4 days | 5 hours
Calibration by fitting the π0 mass for each calorimeter cell.
Last calibration applied in May
Automatisation of online fmDST production
Debugging/ understanding calibration code
Integrating PreShower into calibration

## Slide 19: Conclusion
Very successful automatic calibration and alignment system!
Additional offline and hardware alignments
Many studies done during the last year
Optimisations in performance and speed
Better understanding of our detector
More things to be studied and understood

## Slide 20
Backup

## Slide 21: RICH Mirror Alignment
Anatoly,
Claire,
Paras
RICH1 secondary mirrors in y
RICH1 secondary mirrors in z
DOWN
UP
DOWN
DOWN
UP
DOWN
DOWN
UP
DOWN
UP