## Slide 1
20/06/2016 Paras Naik, Claire Prouve, Anatoly Solomin + more
RICH Mirror Alignment

## Slide 2: Misalignment
Proj. Track position
Real track position
Misalignment
Cherenkov angle resolution / rad
azimuthal angle/ rad
Misaligned mirror:
Aligned mirror:
Identify misalignment:
Misalignments on detector plane
Detector plane
ΔθC(Φ) = θmeas.- θexp.
Cherenkov angle resolution / rad
azimuthal angle/ rad
ΔθC(Φ) = Θyp,s cos(Φ) + Θzp,s sin(Φ)

## Slide 3: Overview of the procedure
Events from HLT1 line

## Slide 4: Run I vs. Run II
Run I:
Offline, after data taking
with Ganga for the Brunel reconstruction
Alignment applied at the end-of-year reprocessing
Run II:
Online: after HLT1 and before HLT2
HLT farm (~1700 nodes)
Alignment runs automatically for each Fill in monitoring mode since end of May
HLT1 lines for each RICH detector  triggers on tracks that populate the outer mirrors

## Slide 5
What’s new in 2016?

## Slide 6: Disentangling mirror-pairs
Each pair of primary mirror p and secondary mirror s has 2 equations:
Magnification factors individual mirror tilts
RICH1 primary mirrors
RICH1 secondary mirrors
Challenge: not enough information to fully constrain the solution
sss
RICH1: 8 equations for 10 unknowns aaa
Rotation of primary mirrors followed by according rotation of secondary mirrors yields same results s
 Need additional constraint
ΔθC(Φ) = Θyp,s cos(Φ) + Θzp,s sin(Φ)

## Slide 7: Disentangling – until 2016
RICH1:
fix primary mirrors, align secondary mirrors
Primary mirrors
Secondary mirrors
Andrew Cook
primary mirrors, secondary mirrors
7
RICH2:
Left half: system of equations linking all mirrors starting from primary mirror 12.

## Slide 8: Disentangling – from 2016
L2 regularization (ridge regression): d
rewrite problem as
Minimize: least square method L2 regularization term
Advantages:
more stable than the previous method
Stable w.r.t. small statistical fluctuations (unlike L1 regularization)
 Fewer iterations needed to converge
Matrix of
magnification factors
Vector of results of fit to histograms
Vector of individual mirror tilts

## Slide 9
Recent results

## Slide 10: First alignment 2016
In the global tag cond-20160517
Started from completely unaligned mirrors
RICH1 Cherenkov angle resolution per iteration of first alignment 2016
RICH2 Cherenkov angle resolution per iteration of first alignment 2016
Fluctuation of single mirror due to not-optimal data sample

## Slide 11: Stability of tilts – RICH1
Mag Down
Mag Up
Changes of mirror tilts wrt current DB
# of alignment run between 24/05 - 19/06

## Slide 12: Stability of tilts – RICH1
Mag Down
Mag Up
Convergence criteria
0.1 mrad

## Slide 13: Stability of tilts – RICH2
Convergence criteria
0.1 mrad

## Slide 14: Stability of Resolution
magnet down
magnet up
magnet down before new DB
Resolutions from refractive index calibration (without HPD image correction).

## Slide 15: More very new features
Different convergence criteria for primary and secondary mirrors in y and z respectively
Possibility to automatically compare output of alignment with another given alignment  during MagUP start from MagUP alignment (which is not in the database currently)  converge within few iterations  calculate the difference to alignment in the current Conditions Database
Iterations needed to converge
6min.
12min.
27min.

## Slide 16: Current ‘monitoring’
https://lbgroups.cern.ch/rich/alignmentview.php
primary
secondary
Tilts in y
Tilts in z
secondary

## Slide 17
Backup

## Slide 18: Resolution
magnet down
magnet up
magnet down before new DB
Without HPD image correction: Degradation of resolution over fill.
 Longer fills in 2016

## Slide 19: New HLT Lines
Track pseudorapidity
Track azimuthal angle / rad
Trigger on tracks that will populate the hardest-to-populate mirror-pairs
usually the very outer mirrors
Other tracks in the events will populate the rest
RICH2
Track pseudorapidity
RICH1
RICH2 line:
p > 40 GeV && χ2 < 2 && 2.65 < η < 2.80
(-2.59 < Φ < -2.49) || ( -0.65 < Φ < -0.55) || (0.45 < Φ < 0.65) || (2.49 < Φ < 2.59)
RICH1 line:
p > 10 GeV && χ2 < 2 && 1.6 < η < 2.04
(-2.65 < Φ < -2.3) || (-0.8 < Φ < -0.5) || (0.5 < Φ < 0.8) || (2.3 < Φ < 2.65)
Need to reconstruct ~10 times less events!

## Slide 20: Magnification coefficients
Magnification coefficients: Translate the tilt on the detector plane into actual mirror tilts
Magnification coefficients are calculated new for each iteration:
Introduce 8 rotations: primary and secondary mirrors rotated around ±y and ±z axis respectively
Rotate about 0.3 mrad ( half the resolution of RICH2)
Reconstruct events for each rotation and evaluate the tilts on the detector plane
Need to reconstruct all events 9 times!
Misalignments on detector plane
Mirror tilts

## Slide 21: Further improvements
Magnification coefficients:
translate the misalignment-on-the-detector-plane into actual mirror tilts
Previously calculated for every alignment for each iteration on data
Tested using the same set for all alignments and all iterations
No significant difference in resulting mirror tilts and procedure 9 times faster!!!
Improved method for fitting histograms:
use same Gaussian width for each slice in phi
Same resulting mirror-tilts and 3 times faster
Δθ/ mrads
Φ angle/ rad